## Slide 1: Monitoring Video, Audio & Anc data in a hybrid SDI – IP world
Steve Holmes
Application Engineer
What You Need to Know for Day-to-Day Operation

## Slide 2: IP is Just Another I/O Interface
Just remember that IP is just another I/O interface: A way to get video, audio, and data to or from a switch. (JB)
  It’s how you do that that has changed.

## Slide 3
Although many broadcasters are transitioning to IP, the majority are going to do so in a piecemeal manner.
With ST-2110, the timing information has been removed from the underlaying hardware layer making the distribution asynchronous.
With current broadcast formats, video must be frame synchronous at the camera’s sensor and at the viewers television screen.
The intermediate IP distribution network is asynchronous but the variance in packet jitter directly affects latency leading to potentially longer video and audio delays than we have come to expect from SDI infrastructures.
Although uncompressed video such as that provided by ST-2110 does map to the active video parts of SDI, two major changes have occurred;
  The PTP and SPG may or may not be the same device
  Signal distribution in IP is asynchronous and multiplexed.
Broadcaster Migrate path to IP
Notes: Furthermore, the PTP distribution relies on phase locked loops to provide synchronization and correctly specified PTP-aware Ethernet switches. Now we have an asynchronous PTP system that has its own variable jitter influenced by Ethernet switches, transmission lines, and terminal equipment, as well as a synchronous SDI system.

## Slide 4: SDI Transmission
In SDI we send Video, Audio and Data all on the same Coax line by line
We send a Field or Frame of Video, the Audio that goes with Field or Frame and the Anc data that goes with that Field or Frame.
HANC
A
U
D
I
O
VANC Data

## Slide 5: IP Transmission
In IP we send Video, Audio, and Data on 3 different IP Multicasts
These different multicasts can be on the same fiber but do not have to be
VANC Data
HANC Audio
-40 Data
-30 Data
-20 Data

## Slide 6: Unicast, Multicast, Broadcast
In an IPv4 network, the hosts can communicate one of three ways:
Unicast
  Sending a packet from one Host to another Host
Broadcast
  Sending a packet from one host to all host in the network
Multicast
  Sending a packet from one host to a selected group of hosts
May I Join
May I Join
May I Join
(Switch)

## Slide 7: SMPTE ST 2110
ST 2110 uses separate video, audio, and metadata as essence payloads, or Flows
Uses essence over RTP/UDP
Uses PTP for synchronization (IEEE1588 with SMPTE ST 2059-2 Profile)
These three IP flows make up your program
There are several parts to ST 2110
Source IP Address
RTP Header
Video Payload
(RFC 4175)
Dest IP Address
RTP Header
Audio Payload
(AES 67)
Source IP Address
Dest IP Address
RTP Header
Metadata Payload
(IETF)
Source IP Address
Dest IP Address
ST 2110-20 Video
ST 2110-30 Audio
ST 2110-40 Data

## Slide 8: Analog Video to SDI
In Analog Video we could hang an O-Scope on the video coax and look at it
We had to come up with a way to look at SDI , take 10 bits make a Pixel out of it put that Pixel on the screen
In Analog Audio we could put an O-Scope on the audio and see the Audio.
We had to come up with a way to grab the channel that we wanted from the data out of the HANC and make an audio waveform out of it.
Things we had to do

## Slide 9: SDI to IP
SDI allowed us to carry the Audio and Captions (and several other things) in the Video payload. New tool sets and new ways were created to look at them.
Well we have done it again.. we have moved everything around, And put it on IP, not just IP but 3 different IP Multicasts,
We needed to find / make new tools to look at Video/ Audio / Data(Captions). And make sure the Video/ Audio / Captions etc. are compatible with being put back to SDI if needed.
We will look at how to do this and see IP and SDI side by side.
We have to do a lot of the same things

## Slide 10: Engineering verses Day to Day Work
IP Trouble shooting;
You need a deep tool set to trouble shoot the IP layer
  IP flow status, Packet Jitter, PTP, PTP timing, Buffer, 2022-7 and more
But that’s not what you need for day to day operations
Day to Day work;
  Waveform, Vector, Captions, SCTE104, Audio, Loudness, compare IP to SDI feed.

## Slide 11: LV5600 and LV7600 IP Features
Engineering Tool Set
IP Status
Packet Jitter
2022-7 Timing
PTP
Status
IP Pattern Generator
Buffer
IP Lip Sync
PTP Timing
Phase Adjustment

## Slide 12: LV5600 and LV7600 SDI Features
Waveform
Vector
EYE Pattern *
Picture
Status
4K Pattern Generator
CineZone
CineLite
Audio - Loudness
CIE
Phase Adjustment
Day to Day Tool Set

## Slide 13: True Hybrid Operation.
SDI A
How to look at both SDI and Ip streams at the same time.
IP C
SDI Status
IP Status

## Slide 14: True Hybrid Operation.
SDI A
IP C
608 Captions
How to look at both SDI and Ip streams at the same time.
608 Captions

## Slide 15: Look at waveforms in the same way
But have tools that will go deeper if needed

## Slide 16: Look at audio in the same way
Look at the audio in the same way we are use to
SDI
Input A
Lissajou
SDI
Input A
Bars
IP
Input C
Lissajou
IP
Input C
Bars
SDI
Input A
Bars
Surround Channels missing

## Slide 17: Audio / Video Delay
Check Audio to Video delay from SDI through IP
SDI A input 0 offset +/-
IP C input -46ms
IP input 4 ms Delay after compensating

## Slide 18: PTP / RTP Timing (Leader)
VANC
HANC
Active Pixels
EAV
SAV
Mbit
V Phase Delay of 21 lines is the delay between EAV and SAV (1080i) (1080p 42 lines)
LV5600 / LV7600
PTP Zero Point same as Black
PTP to RTP
Video RTP Start Point
Notes: EAV – End of Active Video
SAV – Start of Active Video
Mbit – Marker Bit

## Slide 19: PTP to BB Timing (Leader)
PTP to analog BB or Tri reference
Reference
VANC
HANC
Active Pixels
Start of Black Burst and Normal Start of PTP

## Slide 20: PTP to FTP Timing (Leader)
PTP to First packet Time
Reference
PTP to FPT

## Slide 21: ANC Data View

## Slide 22: Side by Side ANC Data

## Slide 23: SDI verses IP Physical layer
SDI we look at CRC errors
In IP we look at RTP errors
  CRC errors will not pass through a IP switch.
Transmission errors – Dropped Data

## Slide 24: View of Errors
Every device may show the errors in a picture a little different, it is all in how they build the picture.
In 1080i one IP packet is about ¼ if a line, that’s how much data will be lost for one packet error.
Some are going break up randomly
Some will have lines of bad pixels jumping all over the place
Some will go to black on the error

## Slide 25: Picture Breakup Slice

## Slide 26: Picture Breakup Pixel Lines

## Slide 27: Picture Breakup Blackout

## Slide 28: Packet Errors
Errored
Data
Good data
No Packet Errors
No Packet Errors
Packet Errors
No Packet Errors
Errored IP frames (Packets) are dropped and not propagated
We need to look at this in a different way
One dropped Packet is about ¼ of a 1080 line.
Data Loss but No Packet Errors

## Slide 29: RTP Errors
Errored
Data
Good data
No RTP Errors
No RTP Errors
Packet Errors
No RTP Errors
We can detect errors using the RTP Sequence
RTP Errors
RTP Errors
Data Loss and RTP Sequence Errors

## Slide 30: Recap
Remember IP is just another IO interface – its how we look at it.
You need tools that will still show you errors that you can relate back to SDI.
You need to be able to see Inputs side by side.
You need timing tools to verify that your SDI and IP are locked to the same clock.
Simple user configurable Multi View screen.

## Slide 31
Thank You
Questions?

## Slide 32: Custom Page Layout
WABE2

## Slide 33: Completely Mappable Inputs
Map any input to IP or SDI input
There are 4 Display engines. 1, 2, 3 or 4 inputs can be on the screen at the same time
Map any input to SDI or IP